## Slide 1
Citations:
Humboldt State University1, Departments of Physics1 and Chemistry2
Joshua Maldonado1, Gynell Higby1, Tanner Hooven1, Benjamin Kafin1,2, Carla Quintero1, Ruth Saunders1
Analyzing Resistance in Carbon Nanotube Networks
Figure 1: Schematic showing source and drain electrode with randomly distributed carbon nanotubes between them.
Figure 2:
Visual representation of the different CNT structures produced by rolling up sheets of graphite along different axes. [3]
Background Information:
The devices that consist of thin-film carbon nanotube (CNT) networks have randomly distributed metallic and semiconducting carbon nanotubes placed in between a source and a drain electrode, as illustrated in Figure 1.
The resistance of a carbon nanotube network is affected by many factors, such as the density of carbon nanotubes in the network, the length and width of the network, and the metallicity of the network. For our purposes, the term metallicity refers to the ratio of metallic carbon nanotubes to semiconductive carbon nanotubes in the generated network. In general though, a carbon nanotube is metallic if electrons can flow freely through the tube when a negative charge is applied. Likewise, a carbon nanotube is semiconductive if the flow of electrons experiences interference, but can still flow through the tube. The metallic properties of an individual carbon nanotube are determined by the physical structure of the tube and the way that the carbons are rearranged, as well as the types of bonds between the carbons.
Abstract:
To inform the applicability of carbon nanotube networks for use as field effect transistors or as biosensors, we have run computer simulations in order to characterize the electrical properties of these networks, and specifically, how the resistance of these networks changes with the metallicity, or the percentage of metallic to semiconducting carbon nanotubes. When running simulations over networks with varying metallicities, we find a trend where the resistance increases to a peak value, then decreases.
Methods:
Along with metallicity, resistance occurs in CNT networks by many mechanisms. One of these mechanisms is known as ballistic transport. This mechanism arises due to the properties of Ohm’s law:
Ohm’s law states that resistance is equal to a physical constant, ⍴, multiplied by the length (L) over the width(W) squared of the wire. Ballistic transport is a by product of this law, stating that when an electrons path does not coincide with the side of a wire, resistance is reduced. This can be represented by the inequality L≤𝜆. Where 𝜆 can be thought of as the electrons mean free path. [1]Though ballistic transport is indeed a contributing factor in determining resistance, more research is needed to determine the extent of the mechanisms for resistance.
A computer model was utilized to simulate these carbon nanotube networks and calculate a network’s resistance. Due to the randomness in how these carbon nanotube networks are formed, each network will have a different resistance value. To calculate the typical resistance values for a network size, for example a CNT network with a length of 20μm and width of 10 μm, we must simulate many networks and use the average resistance value of the networks. After modeling several networks, we see the dependence of the network’s resistance on the metallicity of the network. The plotted results are shown in Figure 3.
Results:
After modeling networks over varying channel lengths and a constant channel width, we found that the network’s resistance peaked at around 30% to 40% metallicity. The resistance is lowest at 100% metallicity, which aligns with accepted literature for CNT networks with only metal-metal junctions. This is even lower than 0% metallicity where we have only semiconducting, or semi-semi junction.
Future Work:
One important aspect of future work would be applying a diameter value to nanotubes within our model, as our CNT’s are currently approximated as one dimensional lines. Implementing this change could further improve the efficacy of our theoretical model to more closely resemble experimental data from literature pertaining to resistance in carbon nanotube networks.
Equation 1. [2]
Figure 3: Metallicity vs Resistance in mega ohms with a CNT density of 2.5 CNT/μm2
Background Information continued:
When a metallic CNT crosses a semiconductive CNT, then a junction is formed that creates optimal electric resistance. Our data shows the correlation between percentage of metallic CNTs in a network and the overall resistance of said network.
[1] Kenji Natori, “Ballistic/Quasi-Ballistic Transport in Nanoscale Transistor”, Applied Surface Science: Volume 254, Issue 19, p (6194-6198) (2008)
[2] Mahdi PourFath, “Numerical Study of Quantum Transport in Carbon Nanotube Based Transistors” Vienna University of Technology. Sec 2.7, (2007)
[3] Pekka Koskinen, “Computational Modeling of Carbon Nanotubes” University of Jyväskylä. (2009)