## Slide 1
Abstract
The burgeoning demand for nanotechnology presents a specific issue in that it requires the production of electronic components at a physical scale that is difficult and costly to achieve. Carbon nanotubes (CNTs) have potential in a wide range of electronics applications (1), but there are many lingering questions about their behavior. This project seeks to use computational modeling to propose a relationship between the number of CNT-on-CNT contacts and the effective resistance of a CNT network as the physical parameters change.
Introduction
Carbon nanotube networks exist most simply as random distributions of nanotubes between a voltage source and drain where each CNT-on-CNT contact acts as a resistor.
This simple model allows for the nano-scale component to be related to macro-scale, traditional circuitry through Equations [1] and [2] which define the resistance of the network as resistors are added in series lengthwise or in parallel widthwise.
Building a physical CNT network requires a significant investment of time and lacks immediate flexibility. The development of a robust computational model with widely customizable parameters allows for the testing of any combination of a number of variables that may impact the performance of the network much more rapidly than could be achieved in a physical lab setting. Previous work using computational modeling has yielded insight into the relationships between each of the various channel parameters, including channel dimensions (2), CNT density (2), and the CNT angle distribution within the channel (3), among others.
Better understanding of the ways that channel properties broadly impact the behavior of a network is essential to defining their behavior in eventual applications.
Citations
(1)
Sun, X.; Chen, T.; Yang, Z.; Peng, H. The Alignment of Carbon Nanotubes: An Effective Route To Extend Their Excellent Properties to Macroscopic Scale. Acc. Chem. Res. 2013, 46 (2), 539–549. https://doi.org/10.1021/ar300221r.
(2)
Jang, H.-K.; Jin, J. E.; Choi, J. H.; Kang, P.-S.; Kim, D.-H.; Kim, G. T. Electrical Percolation Threshold of Semiconducting Single-Walled Carbon Nanotube Networks on Field- Effect Transistor. 2012, 8.
(3)
Behnam, A.; Guo, J.; Ural, A. Effects of Nanotube Alignment and Measurement Direction on Percolation Resistivity in Single-Walled Carbon Nanotube Films. Journal of Applied Physics 2007, 102, 044313. https://doi.org/10.1063/1.2769953.
Methods
The computational program developed takes user inputs for channel length and width; CNT length, density, and angle distribution; and the percent semiconducting vs. metallic tubes. Each CNT is defined within the channel as a line drawn between two points and are randomly generated until the selected CNT density is achieved. Each contact between individual tubes has a resistance value applied depending on the nature of the contact and ultimately the effective resistance and the number of contacts in the channel are calculated.
Previous work involved the scaling of either channel length or width individually and resulted in predictable trends that were in line with circuit theory. However, attempting to establish the presence of a consistent relationship for a channel that simultaneously increases both length and width produced inconsistent data sets that depended on the CNT density that was trialed.
In order to determine the way that the effective resistance scales with increasing length and width, the number of CNT connections were counted at several densities generated across channels of increasing size in order to make an assessment of their comparative rates of formation. Since the number of connections is related to the effective resistance, the connections were used as a proxy for examining the way that series and parallel resistors are added to an expanding channel.
Results and Discussion
Comparison of the slopes of the best fit lines in equivalent trials as shown in Table 1 indicates a degree of suppression in those trials which had a fixed length and varied width vs. those which had a fixed width and varied length. This shows that there is a faster rate of formation of contacts in the direction of the length parameter, corresponding to series connections that are associated with an increase in effective resistance. Inversely, there are less connections being formed in the width direction, which would correspond to parallel connections and a consequent decrease in effective resistance. This is at odds with the original assumption that since the increments of increase in each direction were equal, the rates of formation would be equal.
One mechanism that could explain this suppression in the number of width connections is that as the CNTs approach the edges of the channel their angle distribution is increasingly restricted, leading to less connections between the tubes (3). This mechanism explains the density-dependent relationships between the scaling lengths and widths and the effective resistance, because a lesser rate of formation of parallel connections is more likely to be mitigated by a higher density of CNTs, leading to an eventual decrease in resistance after the channel reaches a large enough size.
Future Work
Future work includes using circuit modelling software to determine if the proposed mechanism is supported by conventional circuit science.
Effect of Channel Size on the Development of Resistance in a Carbon Nanotube Network
David Zeitz1, Carla Quintero2, Ruth Saunders2
Department of Chemistry, Humboldt State University1; Department of Physics and Astronomy, Humboldt State University2
Figure 3: Density dependent relationship between expanding channel dimensions and resistance. Density is measured in CNT/μm2
Table 1: Rates of formation when the channel parameters are fixed as indicated in one dimension and varied from 1-10 microns in the other
Figure 1: Diagram of theoretical CNT network
Figure 2: Code generated CNT network showing contacts
Density | Length 5 | Width 5
6.5 | 58.127 | 68.862
10 | 137.61 | 163.78
Density | Length 10 | Width 10
6.5 | 126.19 | 134.09
10 | 298.69 | 317.87
Equations: Resistance formulas for series [1] and parallel [2] resistors respectively